HP-BASIC  KERMIT USER GUIDE


                 For The Hewlett-Packard Family 9000 Series 200 and 300 Computers

                                   HP-BASIC  WORKSTATIONS


                                         VERSION 1.0


                                       Andrew Campagnola

                                        Hewlett-Packard
                                 Measurement Systems Operation
                              815 SW 14 St. Loveland, Colorado  80537











                                    Copyright (C) 1981,1988
                    Trustees of Columbia University in the City of New York

             Permission is granted to any individual or institution to use, copy,
            or redistribute this document so long as it is not sold for profit.





















                        Kermit-RMB   Table Of Contents


                Section              Topic

                1.0             Kermit-RMB Title Block
                2.0             History Of Kermit-RMB
                3.0             Kermit-RMB Capability Summary
                4.0             Computer System Requirements
                5.0             Using Kermit-RMB
                        5.1     Examples of Kermit-RMB usage
                        5.2     Connecting HP Workstations for Kermit
                        5.2.1   Connecting the 98644 (9 Pin) Interface
                        5.2.2   Connecting the 98626/98628 Interfaces
                        5.2.3   Connecting to Modems
                        5.3     Testing the RS-232 Connection
                6.0             The HP-BASIC File System
                        6.1     Specifying Filenames and Mass Storage
                        6.2     BASIC File Formats
                        6.3     Kermit Handling of Files
                        6.3.1   Sending Files
                        6.3.2   Receiving Files
                7.0             Kermit Program Setup
                        7.1     The Kermit Distribution Disc
                        7.2     Printing the User Manual
                        7.3     Loading and Running Kermit
                        7.4     Minimizing Kermit Program Size
                        7.5     Kermit Initialization File HPK_INIT
                        7.6     Ram Disc Operation
                8.0             Kermit-RMB Command Descriptions
                        8.1     Kermit Command Syntax Reference
                        8.2     Unique Commands for Kermit-RMB
                        8.3     General Kermit Command Groups
                        8.4     Program Management Commands
                        8.5     Local File Management Commands
                        8.6     Terminal Connection and Emulator Commands
                        8.7     File Transfer Commands
                        8.8     Ascii File Transmission Commands
                        8.9     Kermit SET Command Options
                        8.10    Status and Show Commands
                        8.11    Log and Close Commands
                        8.12    Macro Definitions
                        8.13    Kermit Server Commands (Not Implemented)
                        8.14    Remote Server Commands (Not Implemented)
                9.0             Missing Features in Kermit-RMB
                                Future Enhancements
                                Bug Reports







              Kermit-RMB 1.0   Users Manual                                  Page 2





                1.  Kermit-RMB

                This document is available either as an ordinary, plain DOS
                text disk file, or a HP-LIF ASCII file.

                Program:  Andrew Campagnola - Hewlett-Packard Company

                Language:  Hewlett-Packard Series 200/300 BASIC (Rev.  5.x)

                Version:  1.0

                Release:  1 Mar 1989


                2.  History

                This is the first full version of KERMIT for the HP BASIC
                Workstation written.  Keith Moore wrote a BASIC-CSUB which
                implements the KERMIT send and receive protocol for ascii
                files while at New Jersey Division Labs.  His efforts there,
                and a positive response to the availability of his KERMIT for
                HP BASIC combined with the universal need for a native BASIC
                terminal emulator spurred on this project.

                The KERMIT file transfer protocol was developed at Columbia
                University in 1981 under the direction of Frank DaCruz and
                first written by Bill Catchings for CP/M at the Center for
                Computing Activities.  Now over 200 versions of the KERMIT
                program are monitored and supported by that group.

                KERMIT received its name from a muppets poster on the wall
                during the conception of the protocol at Columbia in 1981.
                After attempts to define K-E-R-M-I-T as an acronym failed it
                was admitted that KERMIT was named after KERMIT the Frog with
                Jim Henson's permission.  It was later discovered that KERMIT
                is a Celtic word for "free", and other justifications arose.

                Like all Kermit programs, you are encouraged to use, copy, and
                distribute HP-BASIC Kermit freely.
















              Kermit-RMB 1.0   Users Manual                                  Page 1





           3.       Kermit-RMB Capabilities At A Glance:

           Local operation:                Yes
           Remote operation:               Yes  Requires HP NJD REMCON BIN
           Transfers text files:           Yes
           Transfers binary files:         Yes  (BDAT, ASCII, HP-UX)
           Wildcard send:                  No
           File transfer interruption:     Yes
           Filename collision avoidance:   Yes
           Can time out:                   Yes
           8th-bit prefixing:              Yes
           Repeat count compression:       Yes  - receive only
           Alternate block check types:    No
           Terminal emulation:             VT100
           Communication settings:         Speed, Parity, Echo   (Full duplex only)
           Transmit BREAK:                 Yes
           IBM mainframe communication:    No
           Transaction (Packet) logging:   Yes
           Session logging (raw download): Yes
           Raw upload (Transmit)           Yes
           Act as server:                  No
           Talk to server:                 No
           Advanced server functions:      No
           Advanced commands for servers:  No
           Local file management:          Yes
           Command/init files:             Yes
           Command macros:                 Yes
           Extended-length packets:        No
           Attribute packets:              Yes
           Sliding windows:                No


               Kermit-RMB is a program that implements the Kermit file
               transfer protocol for the entire HP Series 200/300 BASIC
               Workstation family of computers.

               This user manual assumes that you are new to Kermit but
               familiar with the operation of the HP BASIC Workstation and
               ideas of data communication.  A very brief overview is given
               here, but for details consult the early chapters of the
               Kermit User Guide, or Frank DaCruz' book:

                     Kermit, A File Transfer Protocol, by
                     Frank da Cruz
                     Digital Press (1987)
                     order number EY-6705E-DP
                     (phone 1-800-343-8321)

               which also includes excellent background tutorials on
               computers, file systems, and data communication (including
               modems, cabling, etc).




              Kermit-RMB 1.0   Users Manual                                  Page 2




               For further information about obtaining Kermit programs and
               user documentation, write to:


               Columbia University
               Center for Computing Activities
               Kermit Distribution
               612 West 115th Street
               New York, NY  10025  (USA)



           4.0      System Requirements

               Kermit-RMB was developed on a 9816 Workstation using BASIC
               5.1.  The 9816 was configured with 1Mb RAM and a 98626 Serial
               Interface Card. A Memory Volume was not used.

               Kermit-RMB version 1.0 runs on any Series 200/300 computer
               with 1 Mb of memory.  BASIC 5.x is required.  The Operating
               System and Kermit program will load and run in less than 1 Mb
               but without the use of a Memory Volume.

               Kermit will run on any HP serial interface available for the
               Series 200 and 300 computers. These include the following:

               98644    Built-in 25 Pin Serial Interface on the S/310
               98644    Built-in 9 Pin Serial Interface on S/320 and up
               98626    50 Pin Serial Interface Card fro S/200 and S/300
               98628    50 Pin Datacomm Interface Card for S/200 and S/300


               Kermit-RMB implements both Ascii and Binary file transfer as
               well as providing a near complete Kermit user interface.
               File transfer is provided using both KERMIT Protocol Packets
               (SEND-RECEIVE) and raw upload and download (TRANSMIT - LOG
               SESSION).  Aside from the normal functions of Kermit for file
               transfer, Kermit-RMB also provides useful functions such as:


               ASCII file printing to screen and printer     PRINT / TYPE
               A Hex Editor and dump utility                 DUMP
               VT-100 Terminal emulation                     CONNECT
               A File Type Conversion Utility                CONVERT












              Kermit-RMB 1.0   Users Manual                                  Page 3




             5.0   Using Kermit-RMB

               Kermit-RMB performs two major functions, terminal emulation
               and file transfer.  File transfer can be done using either
               the Kermit file transfer protocol (SEND & RECEIVE) , or else
               (without error checking), raw ASCII transmission methods.  To
               use Kermit for "raw" uploading or downloading of files, see
               the descriptions of the TRANSMIT and LOG SESSION commands.

               Two computers use the KERMIT transfer protocol to send files to
               each other by running a KERMIT program on each computer. This is
               an important point - Kermit running on one computer cannot send
               or receive files from another computer running some other file
               transfer program (ie. Xmodem, or HP Advancelink) because the
               protocols (or encoding) used is not the same. Therefore one key
               advantage of using Kermit is that many computers on the market
               have a version of Kermit written for them. You should be aware
               that many terminal emulator programs, especially for the PC
               contain the capability of performing file transfers using a
               variety of protocols, including Kermit. Check into this before
               assuming your terminal emulator cannot support Kermit.

               If you are trying to transfer files to a computer system and do
               not have a Kermit program for that system you should contact
               Columbia University to see if one exists.

               Without Kermit running on each computer, your only other option
               is to use simple ascii transmission which does not "encode" files
               using any protocol.  For example the Kermit Transmit command
               could be used with most any PC Terminal Emulator that performs
               "File Logging".  The disadvantage of using this method is the
               lack of binary file transfers or parity error detection.


               5.1  Kermit - to - Kermit File Transfer

               Once you have obtained versions of Kermit for each computer
               on each end of the file transfer you are ready to begin making
               the RS-232 connection and transferring files. Making the physical
               connection is discussed in the next section after this overview
               of using Kermit.

               There are two scenarios for file transfers I'll discuss here and
               give examples for. One involves transferring files between two
               computers that are next to each other (let's say in the same
               lab), and the other scenario of transferring files between two
               computers that are remote to each other (let's say from a local
               instrument controller to a remote VAX in the computer center
               - or in a remote building accessed via modem).  Remember -
               both scenarios involve an RS-232 connection between the two
               computers that must be established first.


               (1) Local - to - local  File Transfer


              Kermit-RMB 1.0   Users Manual                                  Page 4





               Assume you have connected a Series 300 to a Personal Computer
               in your lab using the HP-24542G Serial Printer Cable (This
               conenection is discussed later). To transfer a file from the
               Series 300 to the PC would involve the following:

           A.  Start each computer, load and run Kermit on each side.

               Kermit comes up on each computer with its local prompt:

               MS-KERMIT> may be the prompt you see on the PC - MSDOS version
               and
               KERMIT-RMB> is the prompt you'll see on the HP side.


           B.  Configure the receiver (PC) and begin the receive process:

               You tell Kermit what to do by issuing commands to kermit at its
               prompt the same way you issue commands to DOS or Unix.

               MS-KERMIT> SET BAUD 9600      (19200 would work also)
               MS-KERMIT> SET TIMER OFF      (Let the sender be the timer)
               MS-KERMIT> RECEIVE

               Kermit on the PC will begin the receive process and you will
               see the Kermit receive screen which shows you the status of the
               file transfer. (The screen may vary depending on the version)

               At this point the MS-Kermit is waiting to receive a "start"
               signal from the sending Kermit (HP side). Normally Kermit will
               wait for a signal for just so long and then "timeout" and quit
               trying to receive a file if it hasn't heard from the sender.
               Since we shut this off by using the SET TIMER OFF command, the
               MS-Kermit will now wait indefinitely for the sender to begin.


            C. Configure the sender (HP) and begin the send process:

               KERMIT-RMB> SET BAUD 9600     (Baud must be identical)
               KERMIT-RMB> SEND TESTDATA:,700

               HP Kermit begins the sending process by displaying the send file
               status screen on the crt. Before actually sending the file the HP
               Kermit will do a few things like make sure the file is really
               there, check the file type and size of the file so it can tell
               the PC Kermit what it will be sending. Then it sends the "start"
               signal that the PC kermit has been waiting for, and the file
               transfer begins.

               The sending Hp Kermit sends the file by "chopping" it into pieces
               about 100 bytes long, putting each piece into a "packet" and
               sending the packet to the receiving Kermit. The receiving Kermit
               unwraps the "file data" from the packet and stores each piece of
               file data into the destination file. When the entire file has


              Kermit-RMB 1.0   Users Manual                                  Page 5




               been sent the sending kermit notifies the receiving end of this
               andthen each side shuts down the file transfer and returns you to
               the local prompt. You should also see some message to the effect
               "file transfer complete" indicating a successful transfer.

               At the prompt you can now issue another command, send or receive
               another file, or quit by entering the "QUIT" command.

               MS-KERMIT> QUIT
               C:>

               KERMIT-RMB> QUIT
               Kermit Done.


             (2) Local - to - Remote File Transfer

               Local to Remote file transfer works identically the same with
               one difference.  You probably don't want to have to walk over
               to the computer center and start Kermit there every time you
               want to transfer a file.  It would be alot easier if you
               could "logon" to the remote computer and give it commands as
               if you were sitting in front of the computer yourself.  In
               order to logon to a remote computer it must be a multi-user
               (multi-tasking no doubt) system.  Unix systems and VAXs are
               probably the most familiar multi-user engineering systems
               that you know of.  In general, Personal Computers do not
               handle remote logon and use.

               To logon to a remote computer you use the terminal emulator
               built into Kermit to start Kermit and a file transfer
               running.  The Kermit command "CONNECT" starts the terminal
               emulator.  Once the file transfer is running on the remote
               computer you exit the terminal emulator by typing the "escape
               sequence", get back to the local Kermit prompt (KERMIT-RMB>)
               and begin the file transfer on the HP end.

               The following example shows this process; the other computer
               is a Unix system, but the method is the same with most
               others.  When you type a command, you terminate it with a
               carriage return, which you can't see in the example.  The
               mysterious "^]c" is Kermit-RMB's escape sequence, which you
               enter by holding down the Control (Ctrl) key and pressing "]"
               (right square bracket), and then typing the letter C.  This
               example assumes the Kermit-RMB program is stored on disk as
               the PROGram file "HPKERMIT".

            Program Dialog:             Explanation:

            LOAD "HPKERMIT",1

            HP-9000 Kermit-RMB  Version 1.0  1 Mar 1989
            ? for help



              Kermit-RMB 1.0   Users Manual                                  Page 6




            Kermit-RMB>set baud 1200    Set the right baud rate.
            Kermit-RMB>connect          Connect as a terminal.

               You will see the terminal emulator screen on the HP system
               with a "modeline" at the bottom telling you the baud and
               terminal settings, and most important, the Kermit escape
               sequence.

               At this point you are connected to the remote system.
               Type a carriage return to get its attention.


            Login: andyc                Login to the host.
            password: xxxxxx            (Passwords normally don't echo.)
            %                           The remote system prompt

            % kermit                    Start the remote kermit program
            C-Kermit>                   The remote Kermit command prompt
            C-Kermit> receive           Start the remote receive program.

            ^]c                         Escape back to the S200/300.

            Kermit-RMB>

               You have now escaped out of the terminal emulator and the
               local HP Kermit prompt is again active. You are still
               connected and logged on to the remote computer, and the
               remote Kermit program is waiting for the "start" signal from
               your end.

            Kermit-RMB> send DATAFILE:,700       send a file.

              (The file is transferred...)

            Kermit-RMB>                  Transfer complete, prompt reappears.


               In this example, the user loads "KERMIT",1 and sees the
               program's herald and its prompt, "Kermit-RMB>".  Then the
               appropriate communication speed ("baud rate") is set, you
               connect as a terminal, and log in to your ID on the Unix
               system.  To start Kermit on the Unix system the command
               kermit is given, and when it starts the C-Kermit prompt
               appears.  You tell it to receive a file by typing the RECEIVE
               command, and then escape back to the S200/300, and tell
               Kermit-RMB to send the file with the SEND command.  After the
               file is transferred, the user would normally connect back to
               the Unix system, exit from the Kermit program there, and log
               out:

            Kermit-RMB> connect      Connect again.
            C-Kermit>quit
            %                        The remote system prompt appears
            % logout                 Logout from Unix or type Ctrl-D.


              Kermit-RMB 1.0   Users Manual                                  Page 7




            ^]c                      Escape back to the S200/300.

            Kermit-RMB>
            Kermit-RMB> quit

               To transfer a file in the other direction, simply exchange
               the "send" and "receive" commands above.  That's the easiest
               and quickest way to use Kermit.  If you have problems getting
               the file transfer to work use the Kermit STATUS command to
               view the current Serial Port settings and look for any
               obvious incorrect settings (port, speed, parity), fix them
               with SET commands (described in Section 8), and try again.

               Many problems can crop up when you attempt to connect two
               unlike systems over RS-232.  If all communication parameters
               appear to be identical, then check the cabling between the
               two systems - this is often the problem.  Next is a quick
               guide to RS-232 Cabling for HP Workstations:






































              Kermit-RMB 1.0   Users Manual                                  Page 8




             5.2  CONNECTING HP WORKSTATIONS For KERMIT

               Below are instructions for connecting the HP Series 200 and
               300 directly to a Personal Computer, modem, or your existing
               data switch.


               HP SIDE:

               There are a few different serial interface connections for
               the HP Workstation:

               1. Built-in 98644 (9 Pin) interface on S/320,330,350,360 or

                  Built-in 98644 (25 Pin) on S/310.

               2. 98626 Plug-in Serial I/O Card (50 Pin) for S/200/300. or
                  98628 Plug-in Datacomm I/O Card (50 Pin) for S/200/300.

               3. Modem Connections
              --------------------------------------------------------------

                Note:

               The following cables and pin diagrams are provided because
               they are existing cable products that you may have available to
               you already. The cables contain wiring which uses modem
               handshake lines to manage the connection. Two computers either
               local or remote can also be "direct" connected using a 3-wire
               connection using pins 2,3 and 7. In this case there is no
               hardware handshake, and you are responsible for manually
               connecting and disconnecting.


            5.2.1   To connect the S/320/330/350/360  9-Pin Port to the
                    Personal Computer 9-Pin COM Port, use:


               HP 92221P   9-Pin Male (HP)  to  9-Pin Female (PC)

               |----------------|                               |-------|
               | HP 320/330/350 | --------  HP 92221P  -------- |  PC   |
               |----------------| (9M)                     (9F) |-------|


               Alternately,
               The S/320 and on come shipped with a 9 Pin - to - 25 Pin
               Serial adapter cable to provide an equivalent of the S/310 25
               Pin Serial Port configuration on the other S/300 computers.

               To connect the S/300 25-Pin Port to a 9 Pin Personal Computer
               interface, use the Vectra PC Serial Printer Cable, or an
               equivalent:



              Kermit-RMB 1.0   Users Manual                                  Page 9






               HP 24542G 25-Pin Male (HP)  to  9-Pin  Female (PC)


               |-----------|                                   |--------|
               | HP 310    | -----------  HP 24542G  --------- |   PC   |
               |-----------| (25-M)                      (9-F) |--------|



               |-----------|    9-->25 Adapter                 |--------|
               | HP 320,30 | <-----------------< <-HP 24542G-< |   PC   |
               |-----------|    HP 98561-61604                 |--------|




               or obtain an equivalent according to the pin assignment
               below:

                  (s/300)  25 Pin Male         9 Pin Female  (PC)

                          (1) Shell ---|
                          (2) TX    ------->    (2) RD
                          (3) RD    <-------    (3) TX
                          (4) RTS   ------->    (1) CD
                       /- (5) CTS   <-------    (4) DTR
                       \- (6) DSR   <--|
                          (7) GND   --------    (5) GND
                          (8) CD    <-------    (7) RTS
                          (9) nc                (9) RI
                          (20)DTR   ------->  /-(6) DSR
                                        |-->  \-(8) CTS
                          (22)RI    ---|


                  The adapter cable for the 9 Pin Built-in HP interface is
                  HP 98561-61604  (9 Pin male to 25 Pin female)

                  9 Pin Male (CPU)      25 Pin Female (equivalent to 310)

                   DTR  (1) -------->   (20) DTR
                   TX   (2) -------->   (2)  TX         The adaptor cable
                   RD   (3) <--------   (3)  RD         just maps the 9
                   RTS  (4) -------->   (4)  RTS        Pin to the 25 Pin
                   CTS  (5) <--------   (5)  CTS        Interface. No
                   DSR  (6) <--------   (6)  DSR        jumpering is done.
                   GND  (7) <------->   (7)  GND
                   CD   (8) <--------   (8)  CD
                   RI   (9) <--------   (22) RI
                   PGND (shell) -----   (shell) PGND
                                |----   (1) PGND



              Kermit-RMB 1.0   Users Manual                                 Page 10






               CONNECTING to 25 PIN PC Interface:


               The HP 13242G Printer Cable (25 Pin - 25 Pin) is used to
               connect from the S/300 25 pin interface to a 25 Pin PC.


               HP 13242G  25-Pin Male (HP)  to  25-Pin Female (PC)


               |----------------|                               |-------|
               | HP 310 (or adp)| --------  HP 13242G  -------- |  PC   |
               |----------------| (25-M)                  (25-F)|-------|


               The HP 92221P cable is equivalent to the combination of the
               adapter (HP 98561-61604) and the 13242G Cable.


             5.2.2.  Connecting to the 98626 or 98628 Interface (50 Pin)


               Both the 98626 and 98628 Serial Interfaces use the 50 to 25 DTE
               Pin Cable (P/N 5061-4215) to provide an equivalent S/300
               25 - Pin Serial Port.

               Once the 50 Pin DTE Cable is used, then the HP 24542H cable
               is used to finish the connection. Below is the
               pin assignment for the 50 Pin and 24542H cables.



             |----------------|    HP 5061-4215       HP 24542H   |-------|
             | S/200  (50-Pin)| <----------------->  >----------< |  PC   |
             |----------------|   50           25      25     9   |-------|



               98626/98628                               24542H

                (50 PIN M)    (25 PIN M)       (25 PIN F)           (PC 9 F)

                 TX      (12) ----> (2)       (2)  TX    ----->    (2) RD
                 RD      (42) <---- (3)       (3)  RD    <-----    (3) TX
                 RTS     (13) ----> (4)       (4)  RTS   ----->    (1) CD    P
           S   * CTS     (44) <---- (5)    /- (5)  CTS   <-----    (4) DTR   C
           /   * DSR     (45) <---- (6)    \- (6)  DSR   <-|
           3     DTR     (14) ----> (20)      (20) DTR   ----->  /-(6) DSR   C
           0                                                |->  \-(8) CTS   O
           0   * CD      (46) <---- (8)       (8)  CD    <-----    (7) RTS   M
                                                            |--    (9) RI
                 RI      (9)  <---- (22)      (22) RI    --|


              Kermit-RMB 1.0   Users Manual                                 Page 11




                 GND     (48) ----- (7)       (7)  GND   ------    (5) GND
                 Shell   (24) ----- (1)       (1)  Shell --|

                 * HW Handshake Lines Used when  'SET HANDSHAKE ON'  is used



           5.2.3. Modem Connections

                                       DCE
             |----------------|    HP 5061-4215       |-------|
             | S/200   50-Pin | <----------------->   | MODEM |
             |----------------|   50           25     |-------|



             |----------------|    HP   ?             |-------|
             | S/300   25-Pin | <----------------->   | MODEM |
             |----------------|   25           25     |-------|



             |----------------|    HP   ?             |-------|
             | S/300    9-Pin | <----------------->   | MODEM |
             |----------------|   9            25     |-------|































              Kermit-RMB 1.0   Users Manual                                 Page 12





             5.3   TESTING THE RS-232 CONNECTION:


               The best way to test the RS-232 Connection is to run the
               terminal emulator on the computer at each end of the
               connection. Although this verifies communication is occuring,
               it does not guarantee that all parameters are set correctly.
               It is safe to assume that baud rate, transmit and receive
               lines, and parity are compatible. This is usually enough to
               allow Kermit to send and receive files. Other issues may
               involve hardware handshake lines (DTR,DSR and RTS,CTS) and
               the number of data bits per frame (7 or 8).

               If nothing occurs after both computers "connect" then Kermit
               provides some very helpful commands for determining the
               problem. Below also is a list of Kermit commands for
               modifying the RS-232 parameters of the Serial Port.


               KERMIT-RMB> CONNECT

               This will start the terminal emulator. If successful, you
               will see a flashing cursor in the upper-left corner of the
               screen, and along the bottom of the screen will appear a
               "modeline" showing the Kermit escape sequence, baud rate,
               data bits setting, parity, and ON or OFF for parity check.
               If this does not occur, then serial communications never
               started - this either indicates that a hardware handshake has
               been enabled and the required modem signals are not present,
               or there is a problem with the serial interface - selftest,
               or operation.

               To correct the problem, return back to Kermit by pressing the
               escape sequence:  CTRL-]

               You will see an 'escape options' line appear along the bottom
               showing the terminal escape options. You complete the escape
               option by typing one of the leters shown.

               Type C to return to kermit.

               At the Kermit prompt use the SET command to shut off
               handshaking:

               < remove the rs-232 cable attached to the serial interface>

               KERMIT-RMB> SET HANDSHAKE OFF
               KERMIT-RMB> SET LOCAL-ECHO ON     Turn on terminal echo
               KERMIT-RMB> CONNECT               Try the connection again


               If there is still no cursor, or echo of the keys you type,
               there is possible indication of a program error - contact


              Kermit-RMB 1.0   Users Manual                                 Page 13




               Kermit Distribution for assistance.

               Once the local terminal emulator is running, try connecting
               the two computers together - attach the rs-232 cable to both
               ports, and run the status command to verify that both Kermits
               are set up correctly:


               1. KERMIT-RMB> STATUS

               Run the status command on each computer. It will list such
               parameters as Baud Rate, Data Bits, Handshake used (RTS/CTS
               etc) Software flow control (XON/XOFF etc). Make sure these
               parameters are identical for each side.

               2. KERMIT-RMB> SHOW  TERM
                  KERMIT-RMB> SHOW  COMM
                  KERMIT-RMB> SHOW  MODEM

               These commands are similar to the status command and show
               parameters related to the command - Comm, Terminal, Modem.

               KERMIT COMMANDS FOR SERIAL PORT CONFIG and DEBUG

               KERMIT-RMB> HELP or ?

               KERMIT-RMB> STATUS

               KERMIT-RMB> SHOW ?   [comm, term, modem ]

               KERMIT-RMB> SET  ?   [baud, parity, handshake, flow, echo ]

               KERMIT-RMB> CLEAR       (resets the serial port)

               KERMIT-RMB> SET PORT ?  (displays the installed cards)





















              Kermit-RMB 1.0   Users Manual                                 Page 14




             6.0   The HP-BASIC File System

               The features of the HP-BASIC file system of greatest interest
               to Kermit users are the form of the file specifications, and
               the formats of the files themselves.

              6.1   File Specifications

               HP-BASIC file specifications  are of the form

                 "/PATHNAME/FILENAME:,7xx,Unit"     (assuming HP-IB 7 used)

               If no path or Mass Storage Specifier (:,7xx,x) is provided
               the current source directory or lif volume is used.  The
               default source and destination directories are set to the
               current MSI when Kermit is run.  To see the settings use the
               STATUS command, and to change them use the SET SOURCE and SET
               DESTINATION commands:


               KERMIT-RMB> STATUS

               KERMIT-RMB> SET SOURCE  :,700,0

               KERMIT-RMB> SET DESTINATION  /KERMIT:,702,0


               When Receiving files the Default DESTINATION MSI is used if
               a msi is not specified as part of the filename specification.
               For sending files the Default SOURCE MSI is used in a similar
               way.

               The device, path, name, and type fields may contain uppercase
               letters, digits, and the special character underscore.


               Illegal characters include all other special characters and
               punctuation including period, colon, and semi-colon.

               Files received with illegal filenames are converted to legal
               LIF filenames by converting illegal characters to underscore,
               and truncating the filename at the maximum allowable length.
               This is 10 Characters for LIF Files and 14 for HFS.

               In Kermit 1.0 all filenames are converted to uppercase when
               kermit receives a send or receive command.


             6.2  File Formats

                HP-BASIC systems store files in 3 "user" file types and with
                two data formats - ON and OFF.  This allows much flexibility
                in the use of the file system, but also introduces some
                complexity as far as handling data files.


              Kermit-RMB 1.0   Users Manual                                 Page 15





                The file types addresed by Kermit-RMB are HP-UX, BDAT, and
                ASCII.  The remaining three - SYSTM, BIN, and PROG are not
                user accessable from Kermit and need to be converted to the
                HP-UX file type in order to be transferred.  This can be done
                using the unique Kermit-RMB command Convert:

                Kermit-RMB> CONVERT prog_file TO HP-UX

                The CONVERT command is discussed in section 8.2 - Unique
                commands for Kermit-RMB.

                A brief description of the user file types may help to sort
                out the complexity.


               FILE TYPE          Written With             Written With
                                  FORMAT ON                FORMAT OFF
               _____________________________________________________________

               ASCII        Same as Format OFF.    LIF ascii undelimited records.
                                                   4-digit length fields start
                                                   each record.

                Ascii will always be stored as length-header undelimited
                string data regardless of number or string representations.
                The FORMAT ON parameter is ignored when ASCII files are
                accessed.


               HP-UX       Identical to DOS Text        Lines and Numbers
                           with CR-LF delimiters        use the null char
                           for each line.               as a delimiter.



               Hp-ux files are handled differently according to the file
               type set in Kermit.  The SET FILE TYPE [binary | ascii]
               command is used to set this indication.


               BDAT        CR-LF delimited lines -      Memory Image of data
                           same as hp-ux but includes   with no delimiters.
                           a 1-sector file header.      The internal data
                                                        is undelimited and only
                                                        decoded if the internal
                                                        file format is known.

                Version 1.0 of Kermit cannot handle mixed intger,real,string
                BDAT files written with Format OFF.  To transfer a BDAT-Format
                OFF file you will need to manually create a file (Format OFF)
                of all integers, or all reals, or convert the file to a BDAT
                Format ON file.



              Kermit-RMB 1.0   Users Manual                                 Page 16




                The File Mode setting in Kermit determines whether the BDAT
                data (format off) is to be converted to ascii numeric
                representation before sending.





















































              Kermit-RMB 1.0   Users Manual                                 Page 17




               6.3 Kermit-RMB handling of files


                Kermit-RMB will open the specified file being sent and
                determine its file type when the file is opened.  Depending on
                the file Mode (ASCII or BIN), the file data will be sent
                accordingly:

                Note: Throughout the Kermit File Handling sections reference
                is made to File Type and File Mode. These two terms should be
                understood clearly before reading further.

                File Type  - Refers to the HP BASIC File Types of ASCII, BDAT
                             and HP-UX. These are the three user file types
                             and are accessable from BASIC programs. The hp-ux
                             file type was just intoduced in BASIC 5.0 for
                             compatibility with the hp-ux and DOS operating
                             systems. Before the hp-ux type was introduced the
                             ASCII type was intended for ascii file
                             compatibility between differing operating
                             systems. BDAT (Binary Data) files allow storage
                             of numeric data in a form quickly accessable by
                             BASIC.


                File Mode -  Refers to the method used by Kermit when sending
                             files. The two Modes are ASCII and BINARY. In
                             ASCII Mode, all transmission is of an ascii text
                             representation. In BINARY Mode the transmission
                             is identical to file contents - which may have
                             been either text or unreadable binary. You will
                             see BINARY referred to also as BIN.


                Changing File Mode

                To make maters confusing, Kermit normally refers to handling
                modes as "file type". The normal kermit command to change mode
                is SET FILE TYPE. In Kermit-RMB the command has been changed
                (aliased) to SET FILE MODE <mode>. In this and other Kermit
                documentation you may see the mode and SET MODE functions
                referred to as file type and SET FILE TYPE.

                Kermit-RMB starts up in ascii mode and can be set this way
                using the set command:

                KERMIT-RMB> SET FILE MODE ASCII

                To set file Mode BINARY the same Kermit command is used:

                KERMIT-RMB> SET FILE MODE BIN


               END-OF-FILE


              Kermit-RMB 1.0   Users Manual                                 Page 18





               Some DOS files use the CP/M convention of indicating the end of
               a file my marking the file with a Control-Z CHR$(26) character.
               If the EOF-MODE is set to CTRL-Z then CHR$(26) will be appended
               to the file as it is sent.  You may want to set this flag when
               sending files to a DOS PC by using the SET EOF ON command.

               The EOF-MODE is ignored when receiving files - the CTRL-Z
               character if sent will remain in the file and show up as a SB
               special character in HP-BASIC.  It can be editied out if not
               needed.

               To set ctrl-Z on or off use the following KERMIT command:

                Kermit-RMB> SET FILE EOF CTRL-Z

                Kermit-RMB> SET FILE EOF OFF







































              Kermit-RMB 1.0   Users Manual                                 Page 19





                6.3.1.  Sending Files


             +  ASCII FILE TYPE


                ASCII MODE

                Contents are treated as text and read from the file line by
                line.  A CR-LF sequence is appended to the end of each line
                before the file is sent.  The receiving Kermit will see
                ascii text delimited with standard CR-LF (^M^J) delimiters.

                BINARY MODE

                ASCII Files are sent the same way regardless of File Mode.



             +  HP-UX FILE  TYPE

                ASCII MODE

                In ASCII Mode HP-UX files are read with Format-ON.
                Therefore HP-UX files are expected to have CR-LF line
                delimiters written with Format-ON.  If the HP-UX file was
                written with Format-OFF, File Mode BIN should be set prior to
                sending the file.

                BINARY MODE

                While sending HP-UX files with BINARY mode set the file is
                read as an image and no delimiters are looked for.  The file
                is transferred as a direct image of the file with no added
                CR-LF item delimiters, or terminators.




             +  BDAT FILE  TYPE

                For BDAT file types the Kermit File Mode (ASCII or BIN) refers
                to the way the file data is transmitted, not the way the file
                is read.  This gives you the option to send BDAT binary image
                data as either ASCII or BINARY.  The Kermit SEND command has a
                special optional form for BDAT files to allow this.


                SEND <BdatFile> [<File Contents Specifier>]


                ASCII MODE



              Kermit-RMB 1.0   Users Manual                                 Page 20




                BDAT files are read according to instructions in the Kermit
                SEND Command line, and the data is converted to ascii strings
                and sent with CR-LF delimiters.

                Kermit assumes that the file was written with Format ON unless
                a special identifier is included with the SEND Command:

                SEND Filename           Will read the file with FORMAT-ON

                SEND Filename INT       Will access the file with Format OFF
                                        and read the file as 16 bit integers.

                SEND Filename REAL      Will access the file with Format OFF
                                        and read the contents as 64 Bit Reals.


                It is up to the Kermit-RMB user to know if the ascii file was
                created and written using a FORMAT-ON or OFF attribute.
                Sending BDAT files written in binary mode (Format off) without
                instructing Kermit will generate the error message, "File
                Contents Not Ascii" and the file transfer will abort.


                In all cases the data read from the file is sent in ascii text
                form.  BDAT Format-OFF data is converted (on the fly) to ascii
                numeral and text data.

                The 1-Sector file header on BDAT files will not be sent with
                the file.

                BINARY MODE

                When sending a BDAT file with BINARY mode set, the contents of
                the file are sent without conversion to ascii numeric
                representation.  If the file was written with Format OFF -
                INTEGER (16 bit) or REAL (64 bit) data, then you must indicate
                this in the Kermit SEND Command Line:

                SEND Filename INT
                SEND Filename REAL
















              Kermit-RMB 1.0   Users Manual                                 Page 21






                6.3.2   Receiving Files

                SYNTAX:

                KERMIT-RMB> RECEIVE [Filetype] [Filename] [File Len] [Recl]


             A. KERMIT-RMB> RECEIVE

                With no optional parameters specified, Kermit makes the
                following defaults:

                File type:       hp-ux
                File Name:       given by sending Kermit
                File Length:     given by sending Kermit, or Default 100Kb
                Recl:            256


                Kermit-RMB will create an HP-UX file type by default.  The
                filename from the sending Kermit wil be used.  If the name is
                an illegal HP-BASIC name then it will be converted to a legal
                name.  name.

                In this example Kermit will use the filename provided by the
                remote Kermit, and use the default DESTINATION MSI when
                creating and storing the file.


                B.  Filetype and Filename

               Kermit-RMB> RECEIVE                   Creates an hp-ux file
               Kermit-RMB> RECEIVE  ASCII            Creates an ASCII File
               Kermit-RMB> RECEIVE  ASCII  NEWNAME
               Kermit-RMB> RECEIVE  BDAT             Creates a BDAT File
               Kermit-RMB> RECEIVE  BDAT   NEWNAME

               Kermit-RMB will create a file with the name specified and if a
               optional file type is provided that file type will be created
               instead of a hp-ux type.


               FILE LENGTH:

               If an HFS file is specified as the destination MSI then no
               filelength needs to be specified. HFS files are extensible, and
               therefore Kermit needs no knowledge about the length of the
               file. If the remote Kermit sends Attribute packets which inform
               the receiving kermit of the current files length, then that
               figure will be used in creating the destination file.

               A problem arises when receiving to a LIF type disc, and neither
               the local kermit user specifies filelength, nor the remote


              Kermit-RMB 1.0   Users Manual                                 Page 22




               Kermit sends an attribute packet for the file length. In this
               case the local kermit will create a destination file of default
               length 100 Kb (if disc or ram volume size permits) and try to
               accomodate the incomming file. If the incomming file is larger
               than 100 Kb then a spill file will be created of 100 Kb and the
               file will continue to be received. This process will continue
               until the file is received, or disc space is consumed. If a
               spill file cannot be created, then an Error message will be
               sent to the sending Kermit which will abort the file transfer.


                INCOMPLETE and DUPLICATE FILES:


                Kermit provides two commands for handling incomplete and
                duplicate files.

                KERMIT-RMB> SET INC [KEEP | DISCARD]

                Depending on the value of this parameter an aborted receive
                (incomplete) file will either be erased (DISCARD) or saved in
                its incomplete form on the disc (KEEP).


                DUPLICATE FILE NAMES:


                KERMIT-RMB> SET FILE WARN [ON | OFF]

                This command instructs Kermit to either OVERWRITE a duplicate
                file, or RENAME the incomming file to a unique filename.  With
                Filewarn ON the file will be renamed.  If Filewarn is OFF,
                then the existing file will be purged before the destination
                file is created.  Loss of data could occur if file warn is
                off, and the receive file process is aborted.

                Kermit-RMB starts up with FILE WARN ON (rename files) and
                INComplete ON (Save aborted files).


                Kermit will receive all files and store them as an identical
                image of the file as it was received.  The file is not changed
                in any way, and End-of-line or end-of-file sequences are not
                appended or stripped off.  Therefore, there is no difference
                in receiving files wheter file type is set to ascii or binary.
                It will be up to the HP-BASIC programmer to understand the
                internal contents of a file in order to understand how it must
                be accessed, and with Format ON or OFF.


             C. The last permutation of the receive command is

                Kermit-RMB> RECEIVE BDAT  ,  50



              Kermit-RMB 1.0   Users Manual                                 Page 23





                This instructs Kermit to use the filename being sent by the
                sending kermit but override the HP-UX file type and create a
                BDAT file type instead.  The 50 instructs Kermit to create a
                file with 50 defined records, and since no record length is
                specified then default of 256 bytes will be used.  The , is a
                place holder for filename.  You can still specify the
                destination MSI by specifying it without a filename


                Kermit-RMB> RECEIVE BDAT :,702,1 , 8


                In this example a BDAT file with record length of 8 bytes is
                created to store the received file.  No file length was
                specified in this example - Kermit depends on the sending
                Kermit to notify the receiver of the proper file size to
                create.  If neither occurs then 391 sectors (100 Kb) is
                created by default.





































              Kermit-RMB 1.0   Users Manual                                 Page 24







               7.0   Program Setup and Invocation

               The HP-BASIC Kermit program can be run from any disk without
               any special installation procedure. All the files start with
               HPK____ to uniquely identify them on Columbia University's
               distribution system. Once received you can rename them.


               7.1  The Kermit Distribution Disc


               The KERMIT Distribution disc contains the following files:

               HPKERMIT        Kermit Program File
               HPK_HELP        Kermit HELP File
               HPK_INIT        Kermit Initialization File
               HPK_DOC         Kermit User Manual
               HPKGET_ME       'GET-ME' ASCII program file with document print
                               instructions
               HPK_MISC        Source Code for compiled sections, and Hex
                               editor (DUMP) utility



               7.2   Printing the Kermit-RMB User Manual


               To print this document (which you've probably figured out by
               now) use the Kermit PRINT Command:

               KERMIT-RMB> PRINT  HPK_DOC:,7xx  701

               Adjust the printer address and file MSI according to your
               system.

               To read the file on the CRT (not recommended) use the type
               command:

               KERMIT-RMB> TYPE  RMBK_DOC:,7xx



               7.3  Loading and Running Kermit-RMB


               To load and run Kermit use the BASIC LOAD Command:


               LOAD "HPKERMIT:,7xx",1

               You will see the Kermit prompt appear and the program banner


              Kermit-RMB 1.0   Users Manual                                 Page 25





               HP 9000  Kermit-RMB
               Version 1.0   1 Mar 1989

               ?  for help

               Kermit-RMB>

               Kermit-RMB> is the Kermit prompt at which you can type any
               Kermit command.

               Kermit-RMB> VERSION              Kermit will echo the version


               You may type Kermit commands repeatedly until
               you are ready to quit the program, using the QUIT command.



               7.4 Minimizing the Kermit Program Size


               Kermit programs usually contain more than just send file and
               receive file code. To minimize the amout of RAM required to run
               Kermit, some functions (subprograms) have been removed from the
               HPKERMIT program and placed in the HPK_MISC file, and the
               HPK_HELP file.  If you are not concerned about program size,
               then these functions can be loaded with the LOADSUB command,
               and connected permanently by re-storing the program again with
               the RE-STORE "HPKERMIT" command.  The following Subprograms
               exist in these files and can be loaded:


               FILE        SUB NAME           COMMAND   Description

               HPK_HELP    SUB Kermit_help    HELP      Kermit Help Command
               HPK_MISC    SUB Hex_edit       DUMP      Debug tool to examine
                                                        files

               The HPK_MISC file also contains the BASIC source code for the
               Kermit Encode_packet and Decode_packet CSUBS in HPKERMIT. These
               are provided in case you want to examine, edit, or recompile in
               the future.

               Minimizing Kermit

               There are also subprograms in Kermit which you may not intend
               to make use of that can be deleted from the main program.
               Following is a list of subprograms and functionality you may
               want to delete from HP Kermit. I suggest you backup the
               HPKERMIT file before modifying it. The number of program lines
                in each subprogram is noted in ().




              Kermit-RMB 1.0   Users Manual                                 Page 26




               Subprogram Name       Functionality

               Terminal  (680)       VT-100 terminal for logging on to remote
                                     computers and starting Kermit there. If
                                     you are using kermit between local
                                     computers only you dont need this.

               Transmit  (140)       Raw ASCII file transmission - not
                                     required if you are only using SEND and
                                     RECEIVE commands

               Convert   (140)       Used with the CONVERT command to convert
                                     file types from ASCII, BDAT, HP-UX, and
                                     PROG.  This command is intended to be
                                     used to convert PROG files to HP-UX, so
                                     they can be sent by Kermit. See section
                                     8.2 for a description of the CONVERT
                                     command.

               Phyread               Used by the Convert and Dump (Hexedit)
               Phywrite              commands to access the disc volume
               Get_vol_info          directory, and disc file sectors.
               Get_file_info




               7.5   Kermit Initialization (HPK_INIT File)


                Upon initial startup, the program looks for a file on the
                system's current MSI called HPK_INIT and if found executes the
                kermit commands in the file.  The HPK_INIT file is a special
                case of a "TAKE" file which is an ascii file containing a
                Kermit Commands. See section 8.1 "Program Management Commands"
                for a description of the TAKE command and writing TAKE files.

                This initialization file may contain command macro
                definitions, communications settings for one or more ports, or
                any other Kermit-RMB commands, and you may create it using any
                text editor capable of saving LIF ASCII files.




            7.6    RAM Disk Operation:

                If sufficient memory exists Kermit will create a RAM Disc and
                use it for transfering and modifying files.

                The file will first be copied to the RAM disc, and then sent
                from there.




              Kermit-RMB 1.0   Users Manual                                 Page 27




























































              Kermit-RMB 1.0   Users Manual                                 Page 28




              8.0    Kermit-RMB Command Descriptions


                During interactive operation, all the edit function keys on the
                keyboard are available to edit the command you are entering. The
                recall key will recall previous commands executed. The command
                line when recalled must stil contain the kermit prompt Kermit-RMB>
                in order to be parsed correctly.



                The notation used in command descriptions is as follows:

                [square brackets]      An optional field.  This field may be
                                       omitted.

                {curly braces}         A list of alternatives, separated by commas.
                                       Choose one of the items from the list.


                The following sections describe all the HP-BASIC Kermit commands.
                Since some command descriptions may contain references to other
                commands that haven't been explained yet, you might find that this
                manual makes more sense on a second reading. Notice that some
               commands can be abreiviated using the first letter of the
               command, for example:

               > SET BAUD 1200          > S B 1200
               > SET FILE TYPE BIN      > S F T BIN
               > QUIT                   > Q

                HP-BASIC Kermit supplies a good amount of the full set of
                Kermit commands.  Commands with asterics are unique to
                Kermit-RMB and not found in other Kermits.  Here's a summary:



              8.1    Kermit-RMB command syntax


               CLEAR                    Reset Serial Port Transfers
            *  CLS                      Clear Screen
               CLOSE,CLO                Close Log File
                  PACKET,PAC,P
                  SESSION,S,S
               CONNECT,C,CON            Start Terminal Emulator
            *  CONVERT
               COPY
               CD, MSI
               DEFINE,DEF
               DELETE,DEL
               DO
               CAT,DIR
            *  DUMP


              Kermit-RMB 1.0   Users Manual                                 Page 29




               ECHO
               EXIT
               HELP,?
               LOCAL
               LOG
                   SESSION,SES
                   PACKET,PAC
               OUTPUT
               PRINT,TYPE
               QUIT,Q
               RECEIVE
                  ASCII,BDAT,HPUX
               RENAME
               SEND
               SET,S

                       BAUD,SPEED,B
                       BLOCK-CHECK
                       DEBUG
                       DELAY
                       DESTINATION,DEFAULT,DES,DEF
                       DUPLEX
                          ON,FULL
                          OFF,HALF
                       ECHO,LOCAL-ECHO
                          OFF,REMOTE
                          ON,LOCAL
                       EOF
                          CTRL-Z,Z,ON
                          NONE,OFF,NO CTRL-Z
                       ESCAPE,ESC
                       FILE,F
                          NAME
                          TYPE,T
                             BINARY,IMAGE,B
                          WARNING,WARN
                          SUPERCEDE
                       FLOW-CONTROL,FLO,FC
                          XON,XOFF,X
                          ENQ,ENQ/ACK
                       HANDSHAKE,HS
                       INCOMPLETE
                          OFF,DISCARD
                          ON,KEEP,K
                       LINE,PORT
                       MARK
                       PARITY
                       RECEIVE,REMOTE
                          END-OF-PACKET,EOP,EOL
                          PACKET-LENGTH,PL
                          PAD-CHARACTER,PC
                          PADDING
                          PAUSE
                          START-OF-PACKET,SOP,MARK


              Kermit-RMB 1.0   Users Manual                                 Page 30




                          TIMEOUT

                       RETRY,RET
                       SEND

                           END-OF-PACKET,EOP,EOL
                           PACKET-LENGTH,PL,LEN
                           PAD-CHARACTER,PC
                           PADDING,PAD
                           PAUSE
                           PREFIX
                              CONTROL
                              8BIT
                              REPEAT,REP
                              TIMEOUT,TIM
                              START-OF-PACKET,SOP
                       TERMINAL,T
                               VT100
                       TIMER

               MACRO
               STATUS
               TAKE
               TRANSMIT
               TYPE
               VERSION

                Commands for TAKE files

               ECHO
               COMMENT                  Comment a macro file




              8.2    Unique commands for Kermit-RMB:


                DUMP  {filespec}

                The file specified is copied to the ramdisc and dumped in
                HEX/ASCII format one sector at a time. I used this to verify
                that binary files were being transferred properly. The
                dump utility also allows you to edit the contents of a disc
                sector and write the modified sector to disc.

                After the first sector is displayed the following keys ae
                active:


                TAB             switches edit cursor from Hex to Ascii Edit

                The following functions require the CTRL key to be held down
                simultaneously:


              Kermit-RMB 1.0   Users Manual                                 Page 31





                +               dumps next sector
                -               dumps previous sector
                /               dumps the directory sector holding that
                                file's directory entry.
                *               returns you to the first data sector of file
                # or N          allows you to specify a sector to be dumped
                Q               quit
                K               convert hex number to decimal,ascii, and
                                Kermit representation.
                P               Dump Alpha Screen to Printer
                H               Display this Help
                space bar       write disc sector to disc (you will be asked
                                to confirm).



              CONVERT  filespec  [TO]  filetype


                KERMIT-RMB> CONVERT  Progfile:,702  hp-ux

                The specified file is copied to the ramdisc and its
                directory entry is changed to the specified filetype. The
                original file is not touched unless it was already on the
                ramdisc.


                Caution:
                This command does not convert the contents of the file!  Only
                the directory entry is changed to the filetype specified.

                For example, converting an ASCII filetype to HP-UX will not
                change the ASCII text length headers to CR-LF text delimiters.


               TRANSFERRING PROG FILES

                Note: The documentation for the SEND command does not indicate
                the ability to send PROG type files. This capability was not
                fully debugged before releasing version 1.0. However, if the
                file specified with the SEND command is a PROG file, it will
                be copied to the ramdisc (the original is not touched),
                converted to an hp-ux file and sent to the receiving Kermit.

                The reason this capability is not documented with the SEND
                command is that getting the file back as a PROG file is not
                100% guaranteed. (Kind of like taking off in a jet without
                landing gear). On some occaisions the file when received back
                would not load correctly or run.

                As soon as this capability is debugged it will be included
                with the next release of Kermit. I didn't want to hold up this
                release any further. If you need this capability, let Columbia


              Kermit-RMB 1.0   Users Manual                                 Page 32




                University, or myself know, and we'll be in touch as soon as
                PROG file transfer is debugged.

                Using a PC Hex Editor and the BASIC Hex editor (which was
                written solely for this purpose) I've determined that the
                original PROG file contents can be sent and received back
                fully in tact. The problem arises in restoring the original
                PROG file directory entry. It appears that the PROG
                directory entry uses some other pointer than the logical
                end of file in marking the file. This pointer is lost
                after the file is sent, so restoring it when the file is
                received is not always possible. I've used the DUMP command
                to edit the PROG directory entry so that the file will load
                and run correctly.

                I believe that the solution may be to send the Directory entry
                along with the file when it is sent, and parse it off when the
                file is received again. Keep in touch.



             8.3     GENERAL KERMIT COMMAND GROUPS


                The Kermit Command descriptions that follow have been broken
                into functional groupings under the folowing categories:

                        8.4     Program Management Commands
                        8.5     Local File Management Commands
                        8.6     Terminal Connection and Emulator Commands
                        8.7     File Transfer Commands
                        8.8     Ascii File Transmission Commands
                        8.9     Kermit SET Command Options
                        8.10    Status and Show Commands
                        8.11    Log and Close Commands
                        8.12    Macro Definitions
                        8.13    Kermit Server Commands (Not Implemented)
                        8.14    Remote Server Commands (Not Implemented)


















              Kermit-RMB 1.0   Users Manual                                 Page 33





              8.4  Program Management Commands


                HELP or ?

                Displays a one screen introduction to frequently used Kermit
                commands and their editing keys, and suggests using the
                question mark command to see the terse list of primary level
                Kermit commands.  Also available are HELP 1-6 screens which
                are described in the general help.


                VERSION

                displays the Kermit-RMB program version number, which you
                should know in case you are reporting bugs or seeking
                technical assistance.


                The EXIT Command

                Syntax:  EXIT or QUIT

                EXIT and QUIT are synonyms for each other.  From Kermit-RMB
                they shutdown the program and reset defaults such as key
                labels on, cursor on etc.

                If you are in the Kermit shell from the terminal escape
                CTRL-]K then EXIT returns you to the terminal session.
                Don't use QUIT to exit the Kermit Shell.


                The serial port RS-232 signals are left alone upon EXIT, so
                that modem connections are not broken.  Kermit-RMB may be
                restarted with the connection intact.  Use HANGUP to
                explicitly break a modem connection; and use SHOW MODEM or
                SHOW COMMUNICATIONS to view the status of modem signals
                CARRIER DETECT, DATA SET (modem) READY, and CLEAR TO SEND.


                The TAKE Command

                Syntax:  TAKE filespec

               The TAKE command gives you way a to collect Kermit-RMB commands
               into a single file, so that you can execute many commands by
               typing a single (TAKE) command.  TAKE instructs Kermit-RMB to
               execute commands from the file that you specify.


               Kermit-RMB>take modem_cmd

               This directs Kermit-RMB to find the MODEM_CMD file, open it,


              Kermit-RMB 1.0   Users Manual                                 Page 34




               execute the commands in it, close it, and return to the
               Kermit-RMB> prompt when done.



                To use the HP BASIC program editor to modify the file use the
                BASIC GET command:

                GET "HPK_INIT"       Warning: Remeber this will erase the
                                             Kermit program from memory.

                The BASIC program editor may be used to create an init file by
                beginning each line with a comment and saving the file as
                ascii.


                As an example of a KERMINIT command file:


                10 !comment -- KERMINIT, HP-BASIC Kermit initialization file

                20 !comment -- Don't overwrite my files!

                25 !set warning on

                30 !!  a double !!  is also a comment

                40 !def HP set par odd,set loc on,set hands xon,set flo -

                50 !none,set tim on ; semi-colon starts a comment

                60 !def modem set port 2, set speed 1200

                70 !comment -- I always start out by connecting to UNIX

                80 !set port 9 !  use select code 9

                90 !set speed 4800 !  a second !  starts a comment

                100 !stop


                INIT files are created with the following rules:

                Line numbers are optional - if used start each line with a !
                mark following the line number.

                End the file with a STOP command.

                !! and comment    are comment lines

                ! separates a command from its comment

                Only comments after the COMMENT command will be echoed to the


              Kermit-RMB 1.0   Users Manual                                 Page 35




                screen when the file is executed.




                The ECHO Command

                Syntax:  ECHO [string]

                The ECHO command writes the string to the screen, without
                adding a carriage return or line feed.  ECHO may be used to
                report progress during execution of a TAKE command file, or
                to issue prompts during the execution of a script.

                ECHO Part one completed...


                The COMMENT Command

                Syntax:  COMMENT text

                The COMMENT command lets you add comments to a TAKE command
                file.  The word COMMENT (or any unique prefix thereof) must
                appear as the first word on the line. Double !! in the take
                file will also act as a comment line.


           8.5   Local File Management Commands

                These commands are executed on your local S200/300, directly
                without having to use the local command before execution.
                This allows you to execute the most common file management
                commands without leaving KERMIT.  All file specifications
                may include device and/or directory fields.  The local file
                management commands are:

                CD , MSI  {path:MSI}

                Changes the current working directory to the given path and
                MSI.  All references to local file management commands will
                refer to the current MSI. Don't confuse this with the
                SET DEFAULT {MSI} which specifies the default path for SEND,
                RECEIVE, TRANSMIT, and LOG commands.

                DELETE , DEL , ERASE  {filespec}

                Deletes the specified file. No wildcards.


                CAT or DIR  [path:MSI]

               Performs a CATalog of the current MSI or the MSI included in
               the command specification.



              Kermit-RMB 1.0   Users Manual                                 Page 36





                SPACE  [MSI]

               Tells how much space is available on the current disc, and what
               the largest contiguous space is on a LIF disc.  The number of
               sectors fragmented on the disc is also reported.


                TYPE or PRINT  filespec  [device]

               TYPE displays the specified local file on the screen.  PRINT
               will print the file to the device specified - ie 1 or CRT,
               701.



            8.6   COMMANDS FOR TERMINAL CONNECTION

                The CONNECT command connects your S200/300 as a terminal to
                the remote system so that you may conduct a session there.

                For completeness, the descriptions below contain copious
                reference to the SET commands, which let you modify all sorts
                of terminal and communication parameters (the SET commands are
                described in a later section).  Kermit-RMB is initially set up
                with the following parameters, so that you only need to issue
                SET commands for those that need to be changed:


                Default Kermit Startup

                PORT 9   Or the lowest serial port select code found.
                         if more than one port is found you will be asked to
                         select one.


                TERMINAL VT102
                SPEED 2400
                PARITY None  (Data Bits 8)
                FLOW-CONTROL None
                HANDSHAKE None
                LOCAL-ECHO Off
                ESCAPE Control-]



                The CONNECT Command

                Syntax:  CONNECT , C

               The CONNECT command establishes an interactive terminal
               connection to the remote system using the currently selected
               communications port with all settings currently in effect for
               that port, emulating the currently selected type of terminal


              Kermit-RMB 1.0   Users Manual                                 Page 37




               which is only VT-100 at this point.

               During CONNECT, the characters you type are sent out the
               communication port, and the characters that arrive at the
               port are displayed on the screen.  If you SET LOCAL-ECHO ON,
               Kermit-RMB itself will display the characters you type on the
               screen.

               Before you issue the CONNECT command, be sure to set the
               correct communication speed (SET SPEED) and any other
               necessary communication parameters (e.g.  SET PARITY, SET
            |  LOCAL-ECHO).  If you have SET DEBUG ON, then received control
            |  characters will be displayed in special notation and no
            |  particular terminal will be emulated.

               In addition characters that are sent to the screen will also
               be recorded in a disk file if you have issued a LOG SESSION
               command.

                The CONNECT command turns your S200/300 into a terminal to
                the other computer.  To get back to the S200/300, type the
                escape sequence followed by the letter C (for "Close
                connection").  Usually the escape character is Ctrl-]
                (Control-Rightbracket).  That means, hold down the Ctrl key,
                press "]", release both, and then type the letter C.

                Kermit-RMB> C      Connect to remote system.

                Conduct terminal session here...

                ^]c Escape back to S200/300.

                Kermit-RMB> Prompt reappears.

                This is called "escaping back".  You can use the SET ESCAPE
                command to change the escape character to something besides
                "^]".

                Escape sequences:

               When you press the escape sequence (CTRL-]) while in the
               terminal emulator, a list of available sequence options is
               displayed on the screen.  Below is a list of these options:

               CTRL-] C    Cancel Terminal Emulation - return to KERMIT-RMB>
                 "    K    Invoke a Kermit Shell - use EXIT to return from
                           the Kermit shell to terminal mode.
                 "    B    Send a BREAK signal out the com port.
                 "    Q    Quit Session logging (raw download) if on
                 "    R    Resume Session Logging if previously
                           discontinued.
                 "    M    Toggle the modeline ON/OFF
                 "    E    Toggle Local-echo



              Kermit-RMB 1.0   Users Manual                                 Page 38





                Escape-Level Commands

               The escape character, normally Control-], is used to regain the
               attention of Kermit-RMB during CONNECT (you can change the
               escape character using SET ESCAPE).  When you type the escape
               character, Kermit-RMB waits for you to follow it with a single
               character command.  For instance, the single character command
               "B" sends a break signal over the serial line.  Typing any
               other character (except the space bar, which is the "null
               command") after the escape character will cause Kermit-RMB to
               beep, but will do no harm.


            ?   Help -- Lists the available single-character commands.
            0   (the digit zero) Transmit a NUL (ASCII 0).
            B   Transmit a BREAK signal.
            C   Close the connection and return to Kermit-RMB prompt level.
            K   Create a Kermit Shell
            M   Toggle the mode line, i.e. turn it off if it is on or vice versa.
            E   Toggle Local-Echo ON/OFF
            Q   Temporarily quit logging the remote session.
            R   Resume logging the remote session.


                When using Kermit to connect two S200/300s "back to back,"
                SET LOCAL-ECHO ON so that when you CONNECT to the other
                S200/300 you can see what you are typing.  You should also
                SET TERMINAL NEWLINE ON, so that that a linefeed will be
                automatically supplied for each carriage return you type.


               TERMINAL EMULATION

               Kermit-RMB emulates a minimal VT-100 terminal, and is the
               only terminal emulation provided. Any escape character
               received will begin decoding of an escape sequence. If a
               valid VT-100 sequence is detected it is executed - if the
               sequence is unknown then the entire sequence is displayed on
               the CRT. Presence of these sequences during a VT-100 terminal
               session will indicate those VT-100 sequences that are not
               implemented.

            |   The Mode Line

               When you first issue the CONNECT command, a message will
               display the status of the terminal line parameters such as
               baud rate, parity, and escape sequence.

                Esc: ^]C  baud: 9600  parity: odd  off



             8.7    COMMANDS FOR FILE TRANSFER


              Kermit-RMB 1.0   Users Manual                                 Page 39





                Kermit-RMB's SEND and RECEIVE invoke the Kermit file
                transfer protocol for error-checked transmission of files
                between Kermit-RMB and another Kermit program on the other
                end of the connection.  There are also commands for "raw"
                transfer of files (no error checking) with systems that
                don't have Kermit programs:  LOG SESSION (for capturing text
                files on your S200/300) and TRANSMIT (for uploading text
                files to the remote system).



                During file transfer, Kermit-RMB normally displays its
                progress on the screen as shown below.  The items in
                the right-hand column are updated more or less at random.


                       File name: TESTDAT
               Bytes transferred: 1460
                   % transferred: 10
                         Sending: In progress

               Number of packets: 74
               Number of retries: 2
                      Last error:
                    Last warning:


                    Kermit-RMB File Transfer Display Screen



               File transfers involving floppy disks will be slow and noisy.
               Hard disks are much faster (and quieter), and RAM disks
               faster still (and totally silent).  But if you store new
               files on a RAM disk, be sure to move them to a real disk
               before turning off your S200/300.

               Before attempting to transfer files to the S200/300, make sure
               you have enough room on the selected device.  Kermit does not
               provide a way for you to change disks during a file transfer.
               However, the Kermit protocol will help you out a by creating
               "spill files" which will hold the file data if the original
               file created is too small to hold the incomming file.  Kermit
               will also attempt to prevent transfer of files that are too big
               to fit in the available space.  Kermit-RMB supports "file
               attributes" exchange, and if the other Kermit supports this
               option too, then the receiving program will check free disk
               space before letting the transfer proceed.

               Other attributes exchanged by Kermit-RMB include the file's
               creation date and time, the system of origin, and the file
               type.  Some of these attributes are implemented.



              Kermit-RMB 1.0   Users Manual                                 Page 40





                The SEND Command

                Syntax:  SEND filespec1  [filetype]

               The SEND command causes a file or file group to be sent from
               the local HP-BASIC system to the Kermit on the remote system.

               Currently Kermit-RMB does not support server commands.

               filespec1 may contain the wildcard characters "*" to match
               zero or more characters within a field If filespec1 contains
               wildcard characters then all matching files will be sent, in
               the same order that HP-BASIC would show them in a directory
               listing.


               If the optional filetype is specified, then only files of
               that filetype will be included in the list of files to be
               transferred.

               If the SEND command is specified by itself on the command line,
               then you will be presented with a valid syntax description help
               on the screen.


                If a file can't be opened for read access, the message

                Cannot access file - blank filename will exit
                /default/file:,msi

               Correct the name of the file you want to send at this time, and
               press enter.


                Once you give Kermit-RMB the SEND command, the name of each file
                will be displayed on your screen as the transfer begins.  Packet,
                retry, and other counts will be displayed along with informational
             |  messages during the transfer, in the style specified by SET
             |  DISPLAY.  If the file is successfully transferred, you will
             |  see "Complete", otherwise there will be an error message.

                Several single-character commands may be given while a file
                transfer is in progress:

             |  ^X (Control-X) Stop sending the current file and go on to
                the next    one, if any.

             |  ^Z Stop sending this file, and don't send any further files.

             |  ^C Return to Kermit-RMB command level immediately without
                   sending any kind of notification to the remote system.
                   (^Z  or even ^E is preferable.)



              Kermit-RMB 1.0   Users Manual                                 Page 41




             |  ^E Like ^C, but send an Error packet to the remote Kermit in
                   an attempt to bring it back to server or interactive
                   command level.

             |  CR Simulate a timeout:  resend the current packet, or NAK
                   the expected one.

                Control-X, Control-Z, and Control-E send the proper protocol
                messages to the remote Kermit to bring it gracefully to the
                desired state.  Control-C leaves the remote Kermit in
                whatever state it happens to be in, possibly retransmitting
                its last packet over and over, up to its retry limit.  You
                should only have to use Control-C in dire emergencies (the
                remote Kermit is stuck, the remote system crashed, etc), or
                at those times when you realize that you have given a file
                transfer command to Kermit-RMB without first having told the
                remote Kermit about it.



                The RECEIVE Command

                Syntax:  RECEIVE [filespec] [filetype] [BDAT Rec Length]

                The RECEIVE command tells Kermit-RMB to receive a file or
                file group from the other system.  The file is stored under
                the name it was transmitted with, except that any illegal
                characters are translated to _.  Kermit-RMB passively waits
                for the file to arrive; this command is not to be used when
                talking to a Kermit server (use GET for that).  You should
                already have issued a SEND command to the remote Kermit and
                escaped back to Kermit-RMB before issuing the RECEIVE
                command.  The RECEIVE command is intended for situations
                where the file name and sending operation originates at the
                other side.

                If the optional filespec is provided, incoming files will be
                stored under that name.  The first incoming file is renamed
                and any additional files either overwrite the first (if FILE
                WARNING is OFF) or are renamed slightly from the filespec
                (digits are added to the end of the filename) if
                     SET FILE WARNING ON
                has been spacified.  The filespec may include any
                combination of the following fields:

                Device MSI    Store the file on the designated device,
                in the current directory for that device.  If no device
                designator is given, store it on the current default device.

             |  Directory path Store the file in the designated directory on
             |  the current disk.  If no path given, store the file in the
             |  current directory.

                File name Store the file under the name given.  If no name


              Kermit-RMB 1.0   Users Manual                                 Page 42




                is given, store it under the name it was sent under,
                converted, if necessary, to suit DOS conventions, and
                modified, if SET WARNING ON, to avoid overwriting any file
                of the same name in the same directory.

                If an incoming file does not arrive in its entirety, Kermit-RMB
                will normally discard it and it will not appear in your directory.
                You may change this behavior by using the command SET INCOMPLETE
                KEEP, which will cause as much of the file as arrived to be saved
                on the disk.

                The same single-character commands are available as during SEND:

             |  ^X Request that the remote Kermit stop sending the current
                   file, and proceed to the next one immediately.  Since
                   this is an optional feature of the Kermit protocol, the
                   remote Kermit might not honor the request.

             |  ^Z Request that the remote Kermit terminate the entire
                   transfer; this is also an optional feature that may or
                   may not be supported by the remote Kermit.

                ^C, ^E, and CR operate in the same way as they do during
                SEND.  In this case, ^E should always do what ^Z is supposed
                to do.

                If WARNING is OFF and you type ^X or ^Z to interrupt the
                transfer, you'll either get a partial new file, or else both
                the old and the new file of that name will be lost,
                depending on SET INCOMPLETE.  In any case, when WARNING is
                off, old files with the same name as incoming files will not
                survive.



              8.8   Commands for Raw Uploading and Downloading

                Kermit-RMB can be used to send files to, or capture files
                from, remote systems that do not have Kermit programs
                available.  No error checking or correction is done, so the
                results can very likely contain corrupted characters, spurts
                of noise, gaps, or extraneous system messages or prompts.
                The command for uploading is TRANSMIT, and for downloading
                LOG SESSION.

             |  To minimize loss of data during these operations, be sure to
             |  SET the FLOW-CONTROL and HANDSHAKE parameters to match the
             |  characteristics of the system on the other end.


                The TRANSMIT Command

                Syntax:  TRANSMIT filespec



              Kermit-RMB 1.0   Users Manual                                 Page 43




               The TRANSMIT command provides a basic raw upload
               facility to send ASCII, BDAT, or HP-UX files to the host
               without packets, error checking, or retransmissions, but
               using all the currently selected communication parameters for
               flow control, parity, etc.  Information is read from the disk
               file a line at a time, sent out the serial port.  A disk file
               line ends with carriage-return-linefeed (CRLF).

                Typically, before using this command to upload a file, you would
                start a text editor (preferably a line-oriented, rather than
                full-screen, editor) on the remote host and put it into text
                insertion mode.  When the file has been completely transmitted,
                you would manually enter the required sequence for getting the
                editor out of text insertion mode, and then make any necessary
                corrections by hand.

                Here's an example for VAX/VMS:


                Kermit-RMB>set flow xon/xoff

                Kermit-RMB>connect                   Connect to VAX.

                $ edt foo_txt                        Start the EDT editor.

                *i Put it into "insert" mode.

                ^]c Escape back to Kermit-RMB.

                Kermit-RMB>transmit foo_txt

                Upload the file a line at a time.  ...  The lines are displayed on
                your screen.

                Kermit-RMB>connect

                When done, connect back to the VAX.

                ^Z Type Ctrl-Z to exit EDT insert mode.

                *exit Exit from EDT to save the file.

                $

                If transmission appears to be stuck, you can wake it up by
                typing a carriage return on the keyboard.  You can cancel
             |  the TRANSMIT command by typing a Control-C.  Control-Z's or
                other control characters in the file may have adverse
                effects on the host.  For this reason, you should use
                TRANSMIT only for files that contain 7-bit printing ASCII
                characters, spaces, tabs, carriage returns, linefeeds, and
                possibly formfeeds.




              Kermit-RMB 1.0   Users Manual                                 Page 44




                The LOG SESSION Command

                Syntax:  LOG SESSION [filespec]

                The LOG SESSION command lets you copy the characters that
                appear on your screen during CONNECT into the specified file
                on the S200/300.  You can use this command to download files
                by displaying (usually with a command like TYPE) the file on
                the remote system while logging is in effect.

                Example:

                Kermit-RMB>LOG SESSION  :,0,0

                Starts a file on the Ram Disc called SES_LOG by default. You
                will need to have the terminal emulator active in order to
                trap activity at the serial port.


                Kermit-RMB>connect

                Any activity appearing at the serial port will now be sent to
                the CRT screen and to the log file SES_LOG.

                If you are connected to a PC for example you can now copy the
                file to the PC Serial port and capture it on the HP side:

                C:\> COPY  TEXTFILE COM1:

                If you were using MS-KERMIT on the PC you could use the
                TRANSMIT command to copy the file to the serial port:


                MS-KERMIT> TRANSMIT  TEXTFILE

                The TRANSMIT command on the PC Kermit sends one line of the
                file each time <enter> is pressed.

                To stop session logging temporarily from the terminal emulator
                you use the "Q" escape option:

                CTRL-] Q       Suspends Session Logging,  but leaves the file
                               open.


                To resume logging use the "R" option:  CTRL-] R

                To close the file and end session logging use the CLOSE
                command at the Kermit prompt:


                CTRL-] C                       Leave the terminal emulator
                KERMIT-RMB> CLOSE SESSION      and close the log file.



              Kermit-RMB 1.0   Users Manual                                 Page 45





                During terminal emulation, the LOG command records all the
                characters that arrive from the remote host in the specified
                file, If you have SET LOCAL-ECHO ON, the characters you type
                will also be recorded.  Logging may be suspended and resumed
                within a terminal session with the CONNECT escape-level
                commands Q and R.



            8.9   The SET Command

                Syntax:  SET parameter [parameter] value

                The SET command establishes or modifies parameters for file
                transfer or terminal connection.  You can examine their
                values with the SHOW or STATUS commands.  The following SET
                commands are available in Kermit-RMB:

                ATTRIBUTES  Controls whether Kermit-RMB uses Attribute
                            packets

                BAUD        Communications port line speed (synonym for
                            SPEED)

                DEBUG        Display packet contents during file transfer

                DEFAULT-DISK Default disk drive for file i/o

                DELAY       Wait number seconds before Sending a file

                DESTINATION Default destination device for incoming files

                DISPLAY     For selecting the type of file transfer display

                END-OF-LINE Packet termination character

                EOF         Method for determining or marking end of file

                ESCAPE      Escape character for CONNECT

                FLOW-CONTROL Enable or disable XON/XOFF

                HANDSHAKE   Half-duplex line turnaround option

                INCOMPLETE  What to do with an incompletely received file

                LOCAL-ECHO  Specify which computer does the echoing during
                            CONNECT

                MODE-LINE   Whether to display a mode line during terminal
                            emulation

                PARITY      Character parity to use


              Kermit-RMB 1.0   Users Manual                                 Page 46





                PORT        Select a communications port

                PROMPT      Change the "Kermit-RMB>" prompt to something
                            else

                RECEIVE     Request remote Kermit to use specified
                            parameters

                RETRY       Packet retransmission threshold

                SEND        Use the specified parameters during file
                            transfer

                SPEED       Communications port line speed (synonym for
                            BAUD)

                TAKE-ECHO   Control echoing of commands from TAKE files

                TERMINAL    Emulation and parameters

                TIMER       Enable/disable timeouts during file transfer

                WARNING     Specify how to handle filename collisions



                The SET commands are now described in detail, in
                alphabetical order.



                SET ATTRIBUTES

             |  Syntax:  SET ATTRIBUTES {ON, OFF}

                Disables or enables use of Kermit file Attribute protocol
                packets, which contain the size, time, and date of files
                transferred with packets.  This command is a safety feature
                so that a small misunderstanding with another Kermit cannot
                block transfers.  SHOW FILE tells whether attributes are on
                or off; they are normally ON.


                SET BAUD, SPEED

                Syntax:  SET BAUD  {baud rate}



                SET DEBUG

                Syntax:  SET DEBUG {ON, OFF}



              Kermit-RMB 1.0   Users Manual                                 Page 47




                With DEBUG PACKET, Kermit will display the actual packets on
                your screen during file transfer.  With the normal file
                transfer display, regular-length packets sent and received
                are displayed in fixed-size slots.

                With DEBUG ON
                control characters are
                displayed in uparrow ("^") notation and characters with the
                8th bit set are preceded by the tilde ("~") sign, and your
                session log (if any) will record 8-bit bytes, rather than
                7-bit ASCII, regardless of SET DISPLAY or SET PARITY.

                SET DEBUG ON turns on both SESSION and PACKET debugging, and SET
                DEBUG OFF turns them both off.


                SET DEFAULT-DISK

                Syntax:  SET DEFAULT-DISK  {MSI}

                Specify the default disk drive to use for file transfer,
                directory listings, and so forth. Use CD or MSI to change
                the current directory for file management commands.


                SET DELAY

            |   Syntax:  SET DELAY number

                Wait the specified number of seconds before starting a file
                transfer.  Intended for use when the other side needs appreciable
                time to become ready, such as rearranging cables, changing
                programs, etc.




                SET END-OF-LINE

                Syntax:  SET SEND END-OF-LINE number

                If the remote system needs packets to be terminated by anything
                other than carriage return, specify the decimal value, 0-31, of
                the desired ASCII character.


                SET EOF

             |  Syntax:  SET EOF {CTRL-Z, NOCTRL-Z}

                Controls how the end of file is handled.  CTRL-Z specifies a
                Control-Z character should be appended to the end of an incoming
                file.



              Kermit-RMB 1.0   Users Manual                                 Page 48





                SET ESCAPE

                Syntax:  SET ESCAPE character

                Specify the control character you want to use to "escape" from
                remote connections back to Kermit-RMB.  On most systems the
                default is "^]" (Control- Rightbracket), which was chosen because
                it is a character you would otherwise rarely type.



                SET FLOW-CONTROL

                Syntax:  SET FLOW-CONTROL {XON/XOFF, ENQ/ACK, NONE}

                Specify the full duplex flow control to be done on the
                currently selected port.  The options are XON/XOFF and NONE.
                The specified type of flow control will be done during both
                terminal emulation and file transfer.  By default, XON/XOFF
                flow control is selected.  XON/XOFF should not be used on
                half-duplex (local echo) connections, or when the other
                system does not support it.  If XON/XOFF is used, HANDSHAKE
                should be set to NONE.



                SET INCOMPLETE

                Syntax:  SET INCOMPLETE {DISCARD, KEEP}

                Specifies what to do with files that arrive incompletely:
                discard them or keep them.  They are normally discarded.


                SET LOCAL-ECHO

                Syntax:  SET LOCAL-ECHO {ON, OFF}

                Specify how characters are echoed during terminal emulation
                on the currently selected port.  ON specifies that
                characters are to be echoed by Kermit-RMB (because neither
                the remote computer nor the communications circuitry has
                been requested to echo), and is appropriate for half-duplex
                connections.  LOCAL-ECHO is OFF by default, for full-duplex,
                remote echo operation.



                SET PARITY

                Syntax:  SET PARITY {EVEN, ODD, MARK, SPACE, NONE}

                Specify the character parity to be used on the currently


              Kermit-RMB 1.0   Users Manual                                 Page 49




                selected port.  You will need to SET PARITY to ODD, EVEN,
                MARK, or possibly SPACE when communicating with a system, or
                over a network, or through modems, concentrators,
                multiplexers, or front ends that require or impose character
                parity on the communication line.  For instance, most HP
                mainframe computers use EVEN or MARK parity; Telenet
                normally uses MARK parity.  If you neglect to SET PARITY
                when the communications equipment requires it, the symptom
                may be that terminal emulation works (well or maybe only
                partially), but file transfer or script INPUT commands do
                not work at all.

                NONE means that no parity processing is done, and the 8th
                bit of each character can be used for data when transmitting
                binary files.  If parity is other than none, then there will
                be 7 data bits.

                If you have set parity to ODD, EVEN, MARK, or SPACE, then
                Kermit-RMB will request that binary files be transferred
                using 8th-bit-prefixing.  If the other Kermit knows how to
                do 8th-bit-prefixing (this is an optional feature of the
                Kermit protocol, and some implementations of Kermit don't
                have it), then 8-bit binary files can be transmitted
                successfully.  If NONE is specified, 8th-bit- prefixing will
                not be requested.  Note that there is no advantage to using
                parity.  It reduces Kermit's file transfer efficiency
                without providing additional error detection.  The SET
                PARITY command is provided only to allow Kermit to adapt to
                conditions where parity is required, or 8-bit transmission
                is otherwise thwarted.

             |  If parity is in use, then the display during terminal
             |  emulation, as well as any session log, will be 7-bit ASCII,
             |  unless you have SET DEBUG ON.



                SET PORT

                Syntax:  SET PORT {number}



                SET PROMPT

                Syntax:  SET PROMPT [string]

                This command allows you to change the HP-BASIC Kermit program's
                prompt to any other string.



                SET RECEIVE



              Kermit-RMB 1.0   Users Manual                                 Page 50




                Syntax:  SET RECEIVE parameter value

                This command lets you modify the ways in which Kermit-RMB
                asks the other Kermit to behave.  That is, it controls the
                file transfer protocol options for packets sent to
                Kermit-RMB by the other Kermit.  The parameters and values
                you specify in the SET RECEIVE command are sent to the other
                Kermit during initial negotiations.


             |  END-OF-LINE number The ASCII value of terminating character
                to look for on incoming packets.  Normally carriage return.
                Use this command if the other Kermit is terminating its
                packets with some other control character.


             |  PADCHAR number Ask the remote Kermit to use the given
                control character (expressed as a decimal number 0-31, or
                127) for interpacket padding.  Kermit-RMB should never
                require any padding.

                PADDING number Ask the remote Kermit to insert the given
                number of padding characters before each packet it sends.
                Kermit-RMB never needs padding, but this mechanism might be
                required to keep some intervening communication equipment
                happy.

                START-OF-PACKET number If the remote Kermit will be marking
                the beginning of packets with a control character other than
                Control-A, use this command to tell Kermit-RMB about it (the
                number should be the decimal ASCII value of a control
                character).  This will be necessary only if the hosts or
                communication equipment involved cannot pass a Control-A
                through as data, or if some piece of communication equipment
                is echoing packets back at you.

                TIMEOUT number Ask the remote Kermit to time out and
                retransmit after the given number of seconds if a packet
                expected from Kermit-RMB has not arrived.  Use this command
                to change the other Kermit's normal timeout interval.


                SET RETRY

                Syntax:  SET RETRY number

                Sets the number of times a packet is retransmitted before
                the protocol gives up.  The number of retries can be between
                1 and 63, and is 5 by default.  This is an especially useful
                parameter when the communications line is noisy or the
                remote host is very busy.  The initial packet of a file
                exchange is given three times as many retries to allow both
                systems to become ready.



              Kermit-RMB 1.0   Users Manual                                 Page 51





                SET SEND

                Syntax:  SET SEND parameter value

                The SET SEND command is used primarily to override
                negotiated protocol options, or to establish them before
                they are negotiated.

                END-OF-LINE number ASCII value of packet terminator to put
                on outbound packets.  Normally carriage return.  Use this
                command if the other Kermit needs its packets terminated
                with a nonstandard control character.

                PACKET-LENGTH number Use this as the maximum length for
                outbound packets, regardless of what the other Kermit asks
                for.  Normally, you would use this command only to send
                shorter packets than the other Kermit requests, because you
                know something the other Kermit doesn't know, e.g.  there's
                a device on the communication path with small buffers.

                PADCHAR number Use the specified control character for
                interpacket padding.  Some hosts may require some padding
                characters (normally NUL or DEL) before a packet, and
                certain front ends or other communication equipment may need
                certain control characters to put them in the right modes.
                The number is the ASCII decimal value of the padding
                character, (0 - 31, or 127).

                PADDING number How many copies of the pad character to send
                before each packet, normally zero.

                PAUSE number How many milliseconds to pause before sending
                each packet, 0-127, normally zero.  This may help
                half-duplex or slow systems prepare for reception of our
                packet.  Padding characters are sent only after the time
                limit expires.

                QUOTE number Use the indicated printable character for
                prefixing (quoting) control characters and other prefix
                characters.  The only reason to change this would be for
                sending a very long file that contains very many "#"
                characters (the normal control prefix) as data.

                START-OF-PACKET number Mark the beginning of outbound
                packets with some control character other than Control-A.
                This will be necessary if the remote host or the
                communication channel cannot accept a Control-A as data, or
                if it echoes back your packets.  The remote host must have
                been given the corresponding SET RECEIVE START-OF-PACKET
                command.

                TIMEOUT number Change Kermit-RMB's normal timeout interval;
                this command is effective only if TIMER is set to be ON; it


              Kermit-RMB 1.0   Users Manual                                 Page 52




                is normally ON, with a default interval of 13 seconds.


                SET SPEED

                Syntax:  SET SPEED rate

                Set the transmission speed (in bits per second, commonly
                called baud) of the currently selected terminal
                communications port to 300, 1200, 1800, 2400, 4800, 9600.
                19200 baud has not been tested.

                Kermit-RMB appears to log packets at an effective rate of
                1200 baud.  Transfers to a 2048 byte buffer allow baud rates
                of about any speed, but the packet decoding will proceed at
                about 1200 baud.  (uncompiled BASIC).


                SET BAUD is a synonym for SET SPEED.




                SET TAKE-ECHO

            |   Syntax:  SET TAKE-ECHO {ON, OFF}

                Specifies whether screen display should occur during
                implicit or explicit TAKE operations on KERMINIT or other
                Kermit-RMB command files, and during evaluation of macro
                definitions by the DO command.  Handy for finding errors in
                TAKE files or macro definitions.


                SET TERMINAL

                Syntax:  SET TERMINAL {type}

                VT-100 is the only terminal available with rev. 1.0


             |  NEWLINE-MODE {ON, OFF}

                ON sends a carriage-return-linefeed combination (CRLF) when
                you type carriage return (CR) during terminal emulation.
                OFF (default) just sends a CR when you type CR.  Useful in
                conjunction with SET LOCAL-ECHO ON when CONNECTing two
                S200/300's back-to-back.

                SET TIMER

                Syntax:  SET TIMER {ON, OFF}

                This command enables or disables the timer that is used


              Kermit-RMB 1.0   Users Manual                                 Page 53




                during file transfer to break deadlocks that occur when
                expected packets do not arrive.  By default, the timer is
                ON.  If the other Kermit is providing timeouts, you can
                safely turn the timer OFF to avoid unnecessary
                retransmissions that occur when two timers go off
                simultaneously.


                SET WARNING

                Syntax:  SET WARNING {ON, OFF}

                Specify what to do when an incoming file is about to be
                stored under the same name as an existing file in the target
                device and directory.  If ON, Kermit will warn you when an
                incoming file has the same name as an existing file, and
                automatically rename the incoming file (as indicated in the
                warning message) so as not to destroy (overwrite) any
                existing one.  If OFF, the pre-existing file is destroyed,
                even if the incoming file does not arrive completely.
                WARNING is ON by default as a safety measure, and the
             |  current setting may be observed in the SHOW FILE display.

                The new name is formed by adding numbers starting at the
                last character of the name.



             8.10    The STATUS and SHOW Commands

                Syntax:  STATUS

                The STATUS command displays the values of all the current
                SET options.  There are currently no operands for the STATUS
             |  command.  Use the SHOW command to see logically-grouped
             |  settings, e.g.  SHOW COMMUNICATIONS, SHOW TERMINAL.


             |  The SHOW Command

                Syntax:  SHOW option

                Most parameters that may be altered with SET commands are
                displayed by the STATUS command.  The SHOW command is used
                for displaying macro definitions, key redefinitions, file
                transfer statistics, translations, and other common
                groupings.

                SHOW COMMUNICATIONS displays the settings of the current
                serial port (port, speed, parity, echo, etc) and the status
                of modem signals Carrier Detect, Data Set (modem) Ready, and
                Clear To Send.

                SHOW FILE displays the file transfer control settings, such


              Kermit-RMB 1.0   Users Manual                                 Page 54




                as the current path, file discard, attributes packets
                on/off, warning, end-of-file convention, etc.

                SHOW KEY allows you to determine a key's identification code
                and what it will send in CONNECT mode, most useful for
                obtaining the identification of a key when SET KEY commands
                will be placed in a TAKE file.  This command can be done
                only interactively (use a ?  to see all defined keys).
                Refer to the SET KEY description for details.

                SHOW LOGGING Displays the names of the session, packet, and
                transaction logs, and tells whether logging is in effect.

                SHOW MACROS [macroname] displays the definitions of all
                currently defined macros, as well as the amount of space
                left for new macro definitions.  A macro name, or
                abbreviation, can be included to restrict the list, e.g.
                SHOW MACRO HP will display the definition of the HP macro,
                and SHOW MACRO X will list the definitions of all macros
                whose names begin with X.

                SHOW MODEM displays the status of the modem signals DSR
                (dataset ready, modem tells the S200/300 that it is turned
                on and in data mode), CTS (clear to send, modem grants the
                S200/300 permission to send data), and CD (carrier detect,
                local modem tells the S200/300 that it is connected to the
                remote modem).  The results may be misleading if your
                asynchronous adapter, or the connector or cable that is
                attached to it, is strapped to supply these modem signals
                itself.

                SHOW PROTOCOL displays the values of the Kermit
                protocol-related parameters, including all the SET SEND and
                SET RECEIVE parameters, plus whether the timer, attribute
                packets, and logging are enabled.

                SHOW SCRIPTS displays the script-related variables.

                SHOW SERVER displays which server functions are enabled and
                disabled.

                SHOW STATISTICS displays counts of characters sent and
                received during file transfers, for both the most recent
                transfer and the entire session, and an estimate of the
                average baud rate while sending and listening.

                SHOW TERMINAL displays the terminal settings, which terminal
                is being emulated, the tab stops, etc.

                SHOW TRANSLATION displays the entries in the 256 byte input
                translation table.  Values are expressed numerically to
                avoid confusion with different display adapters, and the
                command shows only entries for which input and output codes
                differ.


              Kermit-RMB 1.0   Users Manual                                 Page 55







             8.11  The LOG and CLOSE Commands


                Syntax:  LOG {PACKET, SESSION}  [Filespec]
                         CLOSE {PACKET, SESSION,}

                The LOG comman tells Kermit-RMB to record the terminal
                session, or the file transfer protocol packets themselves in
                a log file.  Open log files may be closed (and the
                associated logging disabled) using the CLOSE command.  Open
                log files are also closed when you EXIT from Kermit.

                LOG SESSION is used to record your terminal emulation
                typescript.  It was described above, in the section on file
                transfer.


                The LOG PACKETS Command


                Syntax:  LOG PACKETS [filespec]

                The packet log is for diagnostic purposes and records each
                Kermit protocol packet sent and received in printable
                format.  Control characters are written as caret-letter and
                characters with the high bit set are shown as their 7-bit
                part preceeded by a tilde.  The default filename is
                PKT_LOG.  If you experience difficulty with file
                transfers the packet log is valuable in discovering who said
                what to whom, even though a copy of the Kermit book is
                needed to unravel the meaning of each character in a packet.

            8.12    Macro Definitions

                Like TAKE files, macros provide a way of collecting many
                commands into a single command.  The difference between a
                macro and a TAKE file is that Kermit keeps all its macro
                definitions in memory, and can execute them as many times as
                you like, without having to look them up on disk, whereas
                every time you issue a TAKE command, Kermit has to access a
                disk.  But...  you can have as many TAKE command files as
                you like, and they can be as long as you want, whereas
                Kermit-RMB's memory for storing macro definitions is
                limited.  You can put macro definitions and DO commands for
                them in TAKE files, or for that matter, you can put TAKE
             |  commands in macro definitions.  There is a limit of 25
                defined macros at a time.


                The DEFINE Command



              Kermit-RMB 1.0   Users Manual                                 Page 56




                Syntax:  DEFINE macro-name [command [, command [, ...]]]

                Kermit-RMB command macros are constructed with the DEFINE
                command.  Any Kermit-RMB commands may be included.  Example:

                define telenet set parity zero, set baud 1200, connect

                A macro can be undefined by typing an empty DEFINE command
                for it, like

                define telenet

            |   A macro definition may be up to 255 character long. Use a
                hyphen to continue lines longer than 80 characters.


                The DO Command

                Syntax:  DO macro-name [parameters...]

                A Kermit-RMB macro is invoked using the DO command.  For
                instance:

                Kermit-RMB> DEF TEST  SET BAUD 2400 , LOG PACKET , SEND HEX

                Kermit-RMB> DO TEST


             8.13   Kermit Server Commands

                Kermit Server capability is not implemented in version 1.0



             8.14   Commands for Controlling Remote Kermit Servers

                Kermit Client capability is not implemented in version 1.0

                This functionality in some Kermit programs allows users to
                send commands to the remote computer's operating system for
                execution.















              Kermit-RMB 1.0   Users Manual                                 Page 57




             9.0  Future Enhancements, Missing Features and Reporting Bugs


                The most important missing feature in Kermit-RMB is the Server
                and Client capability. The Server operation allows a "client"
                kermit process to request file send and receive from a remote
                Kermit without having to interact each time to execute the
                Kermit SEND or RECEIVE command. Instead, the remote Kermit is
                issued the SERVER command once after which the GET and RECEIVE
                commands are used to initiate file transfers.

                The REMOTE command group allows you to issue Kermit
                configuration commands to a remote Kermit without having to be
                physically at the remote computer.

                The HOST command group is a set of commands which enable you
                to execute operating systems commands, such as file
                management, on the remote host.

                The following functions in version 1.0 of Kermit-RMB have been
                implemented, but could be more fully implemented in future
                revisions of the program -

                - More complete VT-100 emulator

                - Server/Client Packets (GET, I)

                - More complete HELP facility

                - Complete implementation of the SET SEND and SET RECEIVE
                  commands.

                - Implement half-duplex communication with flow control



                Reporting Bugs

                If you want to report bugs, or more importantly, if you would
                like to submit bug fixes, or enhancements you've made to
                Kermit-RMB you should contact Columbia University Kermit
                Distribution at the Center for Computing Activities, and
                myself at the address on the cover of the users manual or in
                the header of the HPKERMIT program file.

                I'll also request your help in distributing the program and
                documentation to any HP-BASIC users that you know of.









              Kermit-RMB 1.0   Users Manual                                 Page 58